## Slide 1: Execution Time per Instruction
lw $t1, offset($t2)
sw $t1, offset($t2)
add $t1,$t2,$t3
beq $t1, $t2, offset
ps = 10^-12 seconds
Notes: FIGURE 4.26 Total time for each instruction calculated from the time for each component. This calculation assumes that the multiplexors, control unit, PC accesses, and sign extension unit have no delay

## Slide 2: Execution Time in Sequential Implementation
Time required to execute 1000 instructions = 800,000 ps

## Slide 3: Single Cycle vs Pipelined Implementation
The clock cycle must have the same length for every instruction
The longest possible path in the processor determines the clock cycle
Load instruction, which uses five functional units in series: the instruction memory, the register file, the ALU, the data memory, and the register file
Pipelining: “An implementation technique in which multiple instructions are overlapped in execution, much like an assembly line.”
Pipelining improves efficiency by executing multiple instructions simultaneously
Throughput: The total amount of work done in a given time

## Slide 4: The Laundry Analogy - Sequential vs Pipelined Design

## Slide 5: Non- Pipelined vs Pipelined Execution
2400 ps VS 1400 ps
How long 1000
Instructions will take to execute?
Notes: FIGURE 4.27 Single-cycle, nonpipelined execution in top versus pipelined execution in bottom. Both use the same hardware components, whose time is listed in Figure 4.26. In this case, we see a fourfold speed-up on average time between instructions, from 800 ps down to 200 ps. Compare this figure to Figure 4.25. For the laundry, we assumed all stages were equal. If the dryer were slowest, then the dryer stage would set the stage time. The pipeline stage times of a computer are also limited by the slowest resource, either the ALU operation or the memory access. We assume the write to the register file occurs in the first half of the clock cycle and the read from the register fi le occurs in the second half. We use this assumption throughout this chapter.

## Slide 6: MIPS Pipeline
MIPS instructions classically take five steps:
Fetch instruction from memory.
Read registers while decoding the instruction. The regular format of MIPS instructions allows reading and decoding to occur simultaneously.
Execute the operation or calculate an address.
Access an operand in data memory.
Write the result into a register.

## Slide 7: MIPS Pipeline – Five Stages
1. IF: Instruction fetch
2. ID: Instruction decode and register file read
3. EX: Execution or address calculation
4. MEM: Data memory access
5. WB: Write back

## Slide 8: Motivation for Pipeline
Pipelining increases the number of simultaneously executing instructions and the rate at which instructions are started and completed.
Pipelining does not reduce the time it takes to complete an individual instruction. For example, the five-stage pipeline still takes 5 clock cycles for the instruction to complete.
Pipelining improves instruction throughput rather than individual instruction execution time.

## Slide 9
Notes: FIGURE 4.33 The single-cycle datapath from Section 4.4 (similar to Figure 4.17). Each step of the instruction can be mapped onto the datapath from left to right. The only exceptions are the update of the PC and the write-back step, shown in color, which sends either the ALU result or the data from memory to the left to be written into the register fi le. (Normally we use color lines for control, but these are data lines.)

## Slide 10: Pipelined Datapath
For this code:
lw $10, 20($1)
sub $11, $2, $3
add $12, $3, $4
lw $13, 24($1)
add $14, $5, $6
What will happen in all IF Stage?
1- At CC1
2- At CC2
3- At CC3 and so on
What will happen in ID, EX, MEM, WB Stage at each CC?
What is the Content of each pipeline register?
1- At each tick
2- At CC1
3- At CC2 and so on?

## Slide 11: Pipelined Execution
Notes: FIGURE 4.34 Instructions being executed using the single-cycle datapath in Figure 4.33, assuming pipelined execution. Similar to Figures 4.28 through 4.30, this fi gure pretends that each instruction has its own datapath, and shades each portion according to use. Unlike those fi gures, each stage is labeled by the physical resource used in that stage, corresponding to the portions of the datapath in Figure 4.33. IM represents the instruction memory and the PC in the instruction fetch stage, Reg stands for the register fi le and sign extender in the instruction decode/register fi le read stage (ID), and so on. To maintain proper time order, this stylized datapath breaks the register fi le into two logical parts: registers read during register fetch (ID) and registers written during write back (WB). Th is dual use is represented by drawing the unshaded left half of the register fi le using dashed lines in the ID stage, when it is not being written, and the unshaded right half in dashed lines in the WB stage, when it is not being read. As before, we assume the register fi le is written in the fi rst half of the clock cycle and the register fi le is read during the second half.

## Slide 12
Pipeline Diagram
Notes: FIGURE 4.44 Traditional multiple-clock-cycle pipeline diagram of five instructions in Figure 4.43.

## Slide 13: Pipelined Datapath
For this code:
lw $10, 20($1)
sub $11, $2, $3
add $12, $3, $4
lw $13, 24($1)
add $14, $5, $6
Notes: FIGURE 4.51 The pipelined datapath of Figure 4.46, with the control signals connected to the control portions of the pipeline registers. Th e control values for the last three stages are created during the instruction decode stage and then placed in the ID/EX pipeline register. Th e control lines for each pipe stage are used, and remaining control lines are then passed to the next pipeline stage.

## Slide 14: Clock Cycle 5
add $14, $5, $6
For this code:
lw $10, 20($1)
sub $11, $2, $3
add $12, $3, $4
lw $13, 24($1)
add $14, $5, $6
lw $13, 24($1)
sub $11, $2, $3
lw $10, 20($1)
$1
Data of sub $11, $2, $3
add $12, $3, $4
24
[[$1]+20]
Data of lw $10, 20($1)
[$2]-[$3]
[$3]
[$4]
[[$1]+20]
$10
[$3]+[S4]
Data of add $12, $3, $4
lw $13, 24($1)
Address of
add $14, $5, $6
add $14, $5, $6
[$1]
24
$10